## Slide 1
S.no. | Description | SPRNG Transform
1 | Project Capacity | 100MW AC / 120 MW DC
2 | AC:DC Ratio | 1:1.2
3 | Location | Baleedupally(V), Muthyalampally(V), Addakal(V), Mahbubnagar (D), Telangana(S).
4 | Co-ordinates | Latitude: 77.91 N; Longitude: 16.47 S
5 | COD | 23-June-2017
6 | Tariff | INR 5.5949 / kWh
7 | Off-taker | Southern Power Distribution Company of Telangana Limited
8 | Contracted Capacity | 100 MW
9 | System Voltage (DC) | 1000 V
10 | Pitch (Meter) | 6.5 Meter
11 | Tilt Angle | 15 Degree Fixed
12 | Module Type/Make/Capacity | Poly crystalline-Tel sun – 310 Wp, 315 Wp, 320 Wp
 |  | Poly crystalline-JA solar -310 Wp, 315 Wp & 320 Wp
13 | Module per string | 42 Modules (21 Modules in series)
14 | Inverter make | ABB PVS 800 – 1000 kW
15 | Inverter Block | 4 MW (4x1 MW Inverter), 2 MW (2x1 MW Inverter), 1 MW (1x1 MW Inverter)
16 | Nos. of Inverter Station | 27 Indoor Station
17 | Project Area | 580 Acer
18 | Land Parcels | Plot – 1 39MW AC/46.8MWp DC
 |  | Plot – 2 54MW AC/64.8 MWp DC
 |  | Plot – 3 7MWAC/8.4 MWp Dc
19 | Module Cleaning system | 100% pipeline network for water based cleaning system is installed in plant.
20 | MMS Configuration | 2P x 21 Fixed tilt MMS
21 | EPC Contractor | Sterling & Wilson
22 | O&M Contractor | Mahindra Teqo Pvt Ltd